## Slide 1: SolidWorks Assembly Tips & Tricks
Brian McElyea, CSWP
Intuitive Research and Technology Corporation
http://www.irtc-hq.com/
CADFanatic.com

## Slide 2: Assembly Mates
View Mates
  Overview of mates to selected entity
  Shows “path to ground” mates
Use Mate References
  Insert, Reference Geometry, Mate Reference…
  Name Mate References for automatic mates

## Slide 3: Assembly Tools
Use Alt-Drag to Mate Parts (Smart Mates)
  Easily apply single mates
  Use as a pseudo-insert mate for fasteners (create two mates at once)
Use Ctrl-Drag to Copy Parts

## Slide 4: Assembly Tools
Selection Tools
  Volume Select…
  Select Mated To…
  Invert Selection
  Select Suppressed
  Select Internal Components
  Select Toolbox
  Advanced Select
    Very specific: display style; references; etc.

## Slide 5: Assembly Tools (cont.)
Isolate
  Temporarily hide unneeded components
  Easily create multiple Display States
  Works on bodies in multi-body parts too!
Tab to hide
  Doesn’t work in multi-body parts
Unload Hidden Components
Show Hidden Components
Combine Isolate with Show Hidden Components for easy, powerful selection

## Slide 6: Assembly Tools (cont.)
Folders
  Group similar or related entities
  Works for mates
  Allows quick and easy suppression
Tags
  Mark components, mates, and features
  Provides another mechanism for searching
Comments

## Slide 7: Assembly Tools (cont.)
Assembly Visualization
  Mass distribution
  Rebuild Time
  Cost breakdown
  Any custom property can be used

## Slide 8: Assembly Tools (cont.)
Assembly Bill of Materials (BOM)
  Model-Based Definition (MBD)
  Quick overview to check properties or quantities
  Can reuse assembly BOM in drawings

## Slide 9: Assembly Tools (cont.)
Magnifying Glass
  Not strictly an assembly tool; also available in parts
  Allows detailed model inspection/ selections without changing overall view
  Activated with “G” key (default);
  press “G” or click to close
  Magnifying glass follows mouse; use Ctrl+MMB to pan with more control
  Scroll wheel zooms in/out
  Hold Ctrl to select multiple entities
  Alt + scroll wheel sections model normal to screen

## Slide 10: Assemblies - Modeling Practices
Unique Filenames
  Use descriptive names (I usually add the project name as a suffix to the part name when initially designing, i.e., “BRACKET, PROJECT 1.sldprt”)
  Use part numbers
Simple Folder Structure
  K.I.S.S.: Keep It Simple, Stupid!
  Single folder will force unique filenames
Build “Real Life” Assemblies
  Avoid flat assembly structures; use subassemblies
  Flat structures update all mates on rebuild
  Subassemblies only update if necessary

## Slide 11: Sharing Data
Defeature
  Removes detail from a part or assembly & saves the results to a new file with no feature definition/history (i.e., a dumb solid)
  Can preserve assembly motion (certain mates, faces, etc.)
  Can store settings for future use, publish to 3D ContentCentral, or save model as separate file
  Saves assemblies as one file with virtual parts

## Slide 12: Large Assemblies
Use 64-bit OS
As Much RAM as Possible
If on 32-bit OS:
  Watch RAM on video adapter
    32-bit OS’s allocate 2GB RAM/process
    Video RAM is part of that 2GB pool!

## Slide 13: Large Assembly Performance
Settings to Optimize Performance
  Clear “Verification on rebuild” for truly large assemblies
  Tools> Options|System Options|Performance|Assemblies:
    Check “Auto load components lightweight”
    Clear “Always resolve…”
    Personal preference on “Check out-of-date…”
    “Always” on “Resolve lightweight components”
    “Rebuild assembly on load” best answered by experience with a particular assembly
    “Mate animation speed” is “Off”
SOURCE: Building Better Assemblies SWW2010 Presentation by Brian Lindahl, Senior Engineer, CAD_Speed-Up, LLC

## Slide 14: Large Assembly Performance (cont.)
Settings to Optimize Performance (cont.)
  Tools|Options|System Options|Assemblies|Large Assemblies:
    Check “Use Large Assembly Mode…”, and set to a manageable number, roughly between 100 & 500.
    Define your “Large Assembly Mode” with as many of the four selectable choices as possible checked. All improve system speed, can you work with that setting?
SOURCE: Building Better Assemblies SWW2010 Presentation by Brian Lindahl, Senior Engineer, CAD_Speed-Up, LLC

## Slide 15: Large Assembly Performance (cont.)
Settings to Optimize Performance (cont.)
  Tools|Options| Document Properties| Image Quality|Shaded and draft quality HLR/HLV resolution:
    Always keep resolution as low as possible to improve performance; exceptions: extremes in part sizes, graphic presentation of model to an end user.
SOURCE: Building Better Assemblies SWW2010 Presentation by Brian Lindahl, Senior Engineer, CAD_Speed-Up, LLC

## Slide 16: Large Assembly Performance (cont.)
Settings to Optimize View Performance
  Tools|Options| System Options| View|Transitions:
    Set to “Off” to get fastest update possible
      Transitions are just fluff and wow-factor.
SOURCE: Building Better Assemblies SWW2010 Presentation by Brian Lindahl, Senior Engineer, CAD_Speed-Up, LLC

## Slide 17: Large Assemblies – Modeling Practices
Assemblies solve serially in this order:
  Parts & assemblies
  Mates
  Component patterns
  Assembly dependent items
SOURCE: Improving Large Assembly and Drawing Performance, SWW2010 Presentation by Craig Therrien, Product Manager, SolidWorks Corporation

## Slide 18: Large Assemblies – Modeling Practices
Mate Performance in Order of Speed (fast to slow):
  Relation mates (coincident, parallel, etc.)
  Logical mates (width, cam, gear)
  Distance mates
  Limit mates
SOURCE: Improving Large Assembly and Drawing Performance, SWW2010 Presentation by Craig Therrien, Product Manager, SolidWorks Corporation

## Slide 19: Large Assemblies – Modeling Practices
Avoid flat assembly structures; use subassemblies (model should reflect real-life)
  Flat structures update all mates on rebuild
  Subassemblies only update if necessary
Yes, this is important enough to say twice!
SOURCE: Improving Large Assembly and Drawing Performance, SWW2010 Presentation by Craig Therrien, Product Manager, SolidWorks Corporation

## Slide 20: Large Assemblies – Modeling Practices
Work Local!
Large Assembly Mode
Suspend Automatic Rebuilds
  Make all your changes, and then manually rebuild all at once
Quick view/Selective Open
Create simplified configurations of parts/assemblies
  Manually
  Automatically
    Tools, Find/Modify, Simplify…
Use SpeedPak

## Slide 21: Large Assembly Drawings
Display Mode should be Shaded without edges until drawing is complete
Hide behind plane:
  RMB on a plane IN THE VIEW of interest (in the FeatureManager) and choose Hide Behind Plane
  Automatically populate the ‘Components to be hidden’ Dialog with components that reside entirely behind (or in front) of the selected plane
  Not a dynamic setting – if new children components are added behind the plane, these are NOT hidden yet
More views = slower
  Create the views that need work first; complete all work possible; make next view
SOURCE: Building Better Assemblies SWW2010 Presentation by Brian Lindahl, Senior Engineer, CAD_Speed-Up, LLC